## Slide 1: EnMS Management Review
January 31, 2011
Example Management Review Presentation-Industrial
50001 Ready Navigator (https://navigator.industrialenergytools.com) February 2017
© 2017 Georgia Tech Research Corporation and U.S. Department of Energy

## Slide 2: Agenda
Report on previous action items (Mgt Rep)
Energy performance summary (Engineering)
  Energy consumption data
  Energy objectives and targets
  EnPIs & energy performance of SEUs
  Future use and consumption estimates
Legal and other requirements – compliance and changes (Legal)
Improvement opportunities and recommendations (Engineering)
EnMS audit results (Mgt Rep)
Status of corrective/preventive actions (Mgt Rep)
Energy policy (Mgt Rep)
Summary of decisions and actions

## Slide 3: Report on Action Items
Status of actions from previous management reviews |  | 
Action item | Status | Complete
Initiate planning for boiler blowdown reduction project (SEU) | Project plan developed and coordinated with engineering, maintenance and purchasing. Reviewed with COO WRT company strategic plan, budgets, production forecast, materials, energy performance improvement, payback, labor and contractor availability. Project ready to proceed. | 12/22/10
Conduct awareness training for administrative staff | 27 Staff trained 1/11/13 Topics included: What is an EnMS? What is its purpose? Key personnel, energy policy, SEUs, EnPIs, personal roles relative to EnMS, objectives and targets. | 1/11/11
Update energy performance improvement opportunities list | Reviewed prioritized opportunity list with engineering, maintenance, purchasing and COO. Reviewed and confirmed opportunity criteria and ratings. List is up to date. | 1/27/11

## Slide 4
Energy Performance
Summary

## Slide 5: Facility Energy Consumption
Chart: Facility Consumption
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Facility Actual | 6238 | 6647 | 6997 | 6742 | 6685 | 6017 | 5994 | 6820 | 6756 | 6895 | 7197 | 7397
Facility Target | 6004 | 6376 | 6832.1394 | 6438.2663 | 6363.7166 | 5822.6674 | 5858.0447 | 5905.7761 | 5949.4126 | 6130.1805 | 6362.1535 | 6445.001

## Slide 6: Boiler Energy Consumption
Chart: Boiler Consumption
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Boiler Actual | 3506 | 3604 | 3752 | 3719 | 3525 | 3205 | 2935 | 3391 | 3360 | 3728 | 4130 | 4345
Boiler Target | 3371 | 3440 | 3635 | 3532 | 3339 | 3108 | 2875 | 3012 | 3245 | 3543 | 3616 | 3702

## Slide 7: Dryer Energy Consumption
Chart: Dryer Consumption
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Dryer Actual | 2862 | 3043 | 3245 | 3023 | 3160 | 2812 | 2756 | 3059 | 3126 | 3245 | 3332 | 3522
Dryer Target | 2841.753 | 2899.92 | 3064.305 | 2977.476 | 2814.777 | 2620.044 | 2423.625 | 2539.116 | 2735.535 | 2986.749 | 3046 | 3120

## Slide 8: Objectives and Targets Performance Summary
 | 2010 Target (MMBtu) | 2010 Actual (MMBtu) | % Change
Objective: 5% reduction in facility natural gas consumption from 2009 baseline | 74,487 | 80,385 | 2.5% ↑
Target 1: 5% reduction in boiler natural gas consumption | 40,418 | 43,200 | 1.5% ↑
Target 2: 5% reduction in dryer natural gas consumption | 34,069 | 37,185 | 3.7% ↑
Note: See separate handout of corrective action taken to adjust EnPIs
for changes in temperature and production.

## Slide 9: Facility EnPI Performance
Chart: Facility EnPI
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Facility Actual | 10226.3133 | 10447.9723 | 10759.153 | 10253.6649 | 9908.4745 | 9067.2092 | 9585.4616 | 8819.0149 | 8902.5346 | 9076.2019 | 9605.08 | 9831.2983
Facility Target | 9338.2212 | 9916.8052 | 10626.2539 | 10013.6501 | 9897.7005 | 9056.1885 | 9111.2122 | 9185.4504 | 9253.3196 | 9534.474 | 9895.2693 | 10024.1248

## Slide 10: Boiler EnPI Performance
Chart: Boiler EnPI
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Boiler Actual | 5747.5881 | 5664.8853 | 5769.3786 | 5656.0931 | 5224.7378 | 4829.7167 | 4693.5819 | 4384.9384 | 4427.5483 | 4907.3359 | 5511.8772 | 5774.9075
Boiler Target | 5243.0286 | 5350.3466 | 5653.6366 | 5493.4373 | 5193.2579 | 4833.9759 | 4471.5833 | 4684.6639 | 5047.0566 | 5510.5459 | 5624.0853 | 5757.8439

## Slide 11: Dryer EnPI Performance
Chart: Dryer EnPI
| 40201 | 40233 | 40261 | 40291 | 40320 | 40352 | 40382 | 40412 | 40442 | 40473 | 40504 | 40533
Dryer Actual | 4691.8417 | 4783.0871 | 4989.7744 | 4597.5718 | 4683.7366 | 4237.4925 | 4407.3293 | 3955.6256 | 4119.2012 | 4271.541 | 4446.8704 | 4681.0643
Dryer Target | 4419.8731 | 4510.3422 | 4766.0157 | 4630.9676 | 4377.9164 | 4075.0417 | 3769.5447 | 3949.1717 | 4254.6687 | 4645.3902 | 4737.5453 | 4852.6399

## Slide 12: Significant Energy Uses
SEU Identification |  | 
Energy uses exceeding 11,305 MMBtu |  | 
Energy Use | MMBtu | Plant %
Dryer | 22,400 | 21.83%
Boiler | 20,329 | 19.81%
Motors | 17,725 | 17.28%

## Slide 13: SEUs Energy Consumption (%)
Chart: Significant Energy Uses vs. Other Energy Users Energy by % Consumption
| Motors | Dryer | Boiler | Other
 | 0.15677 | 0.32889 | 0.3821 | 0.13224

## Slide 14: SEUs Energy Costs
Chart: Significant Energy Uses vs. Other Energy Users Energy by Cost
| Motors | Dryer | Boiler | Other
 | 473076.991 | 338827.9899 | 393271.2 | 398663.7347

## Slide 15: SEUs Current Energy Performance
Significant Energy Uses Current Energy Performance |  |  |  | 
Significant Energy Use | Relevant Variables | Current Energy Performance | Evaluation Date | Evaluation Basis
Boiler | air/fuel ratio, feed water temperature, production | 75% efficient | 12/30/10 | Stack gas analysis
Dryer | inside air temperature, air/fuel ratio, material moisture content | 80% efficient | 12/30/10 | Stack gas analysis
Motors | voltage, washer load | 55% average load | 1/15/11 | Engineering estimate-Weekly motor amperage measurement

## Slide 16: Future Use/Consumption Estimates
Future Estimates January – March 2011 (prepared 12/30/10) |  |  |  | 
 | Future Energy Use |  | Future Energy Consumption | 
SEU | Use | Estimate Basis | Consumption | Estimate Basis
Boiler | cont’d use of steam boiler | No change in production methods | ↑ to 50,978 MMBtu/yr. Facility ↑ to 94,859 MMBtu and $806,303/yr. | 18% increased production in last 2 quarters due to increased sales
Dryer | cont‘d use of gas dryer |  | ↑ to 43,880 MMBtu/yr. Facility ↑ to 94,859 MMBtu and $806,303/yr. | 
Motors | cont‘d use of motors |  | ↑ to 6,126,614 kWh/yr. Facility ↑ to 11,297,660 kWh and $1,027,222/yr. | 

## Slide 17
Energy Performance
Improvement Opportunities

## Slide 18: Top Improvement Opportunities
 | Opportunity Ratings |  |  |  | 
Description of Opportunity | Expected Annual $ Savings | Expected Time to Implement | Simple Payback | EHS Impact | Total Score (x)
Reduce boiler blowdown | 3 | 3 | 4 | 4 | 144
Use synthetic lubricants on compressors | 1 | 3 | 3 | 4 | 48
Recover heat from boiler blowdown | 3 | 1 | 4 | 3 | 36
Replace 40W tubes with 36W EE tubes in office areas | 1 | 3 | 4 | 3 | 36

## Slide 19: Improvement Opportunity Recommendations
Initiate implementation of boiler blowdown reduction project
Implement heat recovery from boiler blowdown
  Minimal time to implement
  Good expected annual savings
  Excellent payback
  Best option in view of current focus on increased production to meet customer demand

## Slide 20
Status Reports

## Slide 21: Status of Legal Requirements
 | Status
Compliance with legal requirements | Compliance audits conducted 3rd Quarter 2010. No negative findings. Currently in compliance with applicable legal requirements.
Changes in legal and other requirements | Maintenance is currently monitoring County Commission consideration of proposed ordinance relative to automatic control of exterior lighting.

## Slide 22: Status of 2010 EnMS Audits
Chart: 
| January | February | March | April | May | June | July | August | September | October | November | December
Planned | 0 | 0 | 0 | 1 | 4 | 8 | 11 | 11 | 16 | 20 | 21 | 21
Conducted | 0 | 0 | 0 | 1 | 4 | 7 | 12 | 12 | 12 | 17 | 18 | 19

## Slide 23: EnMS Audit Results
Nonconformities: |  |  | 
Date | Major | Minor | Comments
12/19/10 | 0 | 3 | 2 findings related to documentation;
 |  |  | 1 finding related to main dryer operational controls
Positive findings:
1. CCTVs in break rooms now run “Energy Tips” videos produced by the Energy Team, supporting internal communications on energy conservation.
2. All energy data now loaded into new Corporate software package which will manage monthly reporting and GHG calculations.

## Slide 24
Chart: Open Action CPARs Graphic shows month in which the action is/was due.
September | 2
October | 4
November | 1
December | 3
January | 1
Status of Corrective and Preventive Actions

## Slide 25: Energy Policy
As an energy intense manufacturer of specialty glass, XYZ Inc. strives to reduce its energy consumption and costs and promote the long-term environmental and economic sustainability of its operations. We are committed to:
Reduce energy consumption in our manufacturing operations
Ensure continual improvement in our energy performance
Deploy information and resources to achieve our objectives and targets
Uphold legal and other requirements regarding energy
Consider energy performance improvements in design and modification of our facilities, equipment, systems and processes
Effectively procure and utilize energy-efficient products and services

## Slide 26: Summary of Decisions and Actions

## Slide 27
Next Management Review
April 30, 2011